## Slide 1: HelperTech
Snow Removal Robot – RoboBlow
April 18, 2011

## Slide 2: HelperTech Members
Leo Cheng (CEO)
  Software Design & Development
YuYuan Liu (VP Operations)
  Software Design & Development
Peter Hsiao (CFO)
  Hardware Development (Mechanical & Electrical)
Joseph Shen (VP Marketing)
  Hardware Development (Mechanical & Electrical)

## Slide 3: Outline
Team Members
Introduction
System Overview
Software
Hardware
Financial & Marketing
Future Development
Question
Demo

## Slide 4: Household Snow Removal
Snow Shovel
Snow Blower
Anti-Icing Chemical

## Slide 5: Limitation: Outdoor
Hazardous Weather
Slippery Ground

## Slide 6: Product Goal
Snow Removal Robot
  Snow Blower (Completed)
  Salt Spraying (Incomplete)
Wireless Remote Control
Real-time Video
Safety Consideration
  Emergency Stop

## Slide 7: System Overview
LED
LCD Screen
Button & Joystick Input
Cameras
Snow Blower Switch
Wheel Control
Camera Direction Control
Snow-out Direction Control
Wi-Fi
Input Signal
Video
Video
Robot State
Control Signal
Control Signal
MCU
MCU
Snow Removal Robot
Controller
Arduino

## Slide 8
Software
Goals and objectives
Software system overview
Details of components

## Slide 9
The robot can be controlled wirelessly by our remote controller
Real-time image can be displayed on the remote controller. Views from different cameras can be switched.
Snow out direction can be controlled by our remote controller.
Safety design
Goals and Objectives

## Slide 10: Software System

## Slide 11: Details of components
Armv9 processor
    video processing
    complete communication protocol
    multi-tasking , Linux program.
    better driver support
    lack of PWM output pins

## Slide 12: Armv9 processor and development board
Image source: http://www.arm9board.net/sel/prddetail.aspx?id=352&pid=200

## Slide 13: Details of components
Arduino (Mega)
    lots of PMW output pins
    easy programming
    suitable to be a slave
Image source: http://arduino.cc/en/Main/ArduinoBoardMega

## Slide 14: Details of components
Webcam
    Mircovim webcam. Linux Driver is built in the kernel.
WIFI Module
    Ralink rt73 chip. Driver and relevant tools are cross-complied by ourselves.

## Slide 15: Details of components
USB joystick
    We bought USB controller breadboard, buttons and direction controller and assembly them together according to our design.

## Slide 16: Hardware – Goals and Objectives
-The snow thrower can be switched on/off wirelessly
-The snow can be blown into desired direction
-The robot can be driven to desired location wirelessly
-The monitoring cameras can be rotated wirelessly
-The robot can move on icy surface (traction)
-Safety features

## Slide 17: Hardware – System Overview

## Slide 18: System Overview
Snow intake (clearing): up to 15.2 cm
Power requirement: 1680 Watt maximum
Total weight: ~ 40 Kg
Frame material: Aluminum & Acrylic boards
System Inputs:
  - Power supply from home outlet
  - Remote control signals via Wi-Fi
System Outputs:
  - Robot motion
  - Snow thrower -> snow removal
  - Snow thrower -> snow blowing direction control
  - Camera orientation control

## Slide 19: System Overview – Structure -Robot base & frame -Robot case & frame

## Slide 20: System Overview – 1st Layer
Includes:
- Power extension cord
- Power outlets
- ATX power supply
- 2x geared DC motors
- Power switch circuit
- Snow thrower
- 2x rubber wheel of 8’’ in diameter
-2x supporting wheels

## Slide 21: System Overview – 2nd Layer
Includes:
- ARM development board
- Arduino microcontroller (slave)
- DC motor driver circuit
- Stepper motor control circuits
- 0.33Amp stepper motor
- 4 Amp stepper motor

## Slide 22: COST ANALYSIS
ARM Development Board x2 | $215
Webcam Camera x2 | $30
NPC DC Gear Moto set (K24466)x2 | $575
Yardworks 9A Sow Thrower | $172
Arduino Microcontroller x2 | $70
Aluminum Welding | $700
White Acrylic Board x3 | $70

## Slide 23: COST ANALYSIS
ATX 600W Power Supply | $50
Extension Chord+ Multi Power Plugs | $90
0.33A Bipolar Mercury Stepper Motor | $27
4A Bipolar Mercury Stepper Motor | $37
Glue Gun, PCB Boards, Screws and Other Tools | $30
H-Bridge DC Motor Driver | $160
WIFI Adaptor | $30
Joystick s+ Control Button | $5
Electronics (Wire+ Heat Sinks + Transistors) etc | $246
TOTAL | $2507

## Slide 24: COST ANALYSIS
Comparing to the proposed cost budget, we are over-budgeted by $1200.
Originally proposed budget:

## Slide 25: TEAM WORK
Divided Into Group Of Two
Software Team: Leo and Yuyuan
Hardware Team: Peter and Joseph
Peter and Yuyuan are in charge of the communication between two teams
The team have regular meeting on a weekly basis

## Slide 26: Timeline Accomplished
Proposed Timeline:

## Slide 27: Timeline Accomplished
Troubles Met:
Underestimated the Difficulty of Dealing With High Power Motor
2. Struggled Finding Right Component that Would Do the Job
3. Had to Omit the Salt Spraying Unit and Cable Automation
Therefore, The First Integration Was Greatly Delayed

## Slide 28: Timeline Accomplished
Real Timeline:
Chart: 
| Motors able to move | Control Wheel's direction/speed | power switch for snow thrower | snow thrower direction | power distribution circuit | Camera processing | motors for camera | First Integration | Wireless communication | Final Integration | Robot Body Complete
START_DATE | 40568 | 40608 | 40573 | 40582 | 40610 | 40593 | 40588 | 40611 | 40594 | 40637 | 40634
DURATION(DAYS) | 40 | 10 | 8 | 7 | 25 | 20 | 5 | 7 | 30 | 10 | 8

## Slide 29: Future Development
Traction
  The current wheels are definitely not suitable for slippery surfaces (budget and time constraints)
  Potential improvements:
    Snow chains
    Glue treads onto the wheel surfaces
    Add two more driving motors and replace the wheels with caterpillar tracks
Snow thrower leveling
  The current design is not adequate for bumpy road conditions.
  Potential improvements:
    Add two stepper motors to adjust the level of the snow thrower so it can be slid up/down along the supportive bars

## Slide 30: Future Development
Cable Automation
  The cable would get in the way of the robot while it’s moving from time to time, causing difficulty for the robot to function properly.
    Potential Improvement:
  Design an automation unit with motor and sensor, to pull/release the extension cable to make sure that the cable is not in the way.
  buy retractable power extension cord, there are alot of options on the market, but we don't really have any budget left

## Slide 31: Future Development
Improve video processing speed
  The current video processing speed is not fast enough to be real-time displayed on the LCD. The possible problem is due to the Wi-Fi speed and the size of the video frame
Extra Functionality
  Salt Spraying
  Motion Sensor
  Positioning System
  AI
Cost Reduction

## Slide 32: Question?

## Slide 33: Controller Layout